## Slide 1: WMOPS -
J. Dailey, J. Bauer, T. Grav, A. Mainzer, R. Cutri, J. Myers, J. Masiero, R. McMillan, S. Gomillion, R. Jedicke, L. Denneau, R. Walker, E. L. Wright, and the WISE Team
Clean Detections of Newly Discovered Solar System Objects by WISE

## Slide 2: WISE Spacecraft
Successful launch on Dec 17, 2009
HgCdTe + Cryogenically cooled Si-As detectors
4 Bands at 3.4, 4.6, 12 and 22 mm
Polar orbit: completes a full orbit (2 scans) every 92min., progresses 2 deg in ecliptic longitude/day
Coverage of at lease 8 frames at the equator, denser coverage at the poles, ~10 frames per region of sky on average
CAVEAT… scans don’t progress linearly, they do a 4-pattern jump and have additional offsets to avoid the Moon.

## Slide 3: WISE & NEOs
Detection & Characterization of Near Earth Objects primary motivation
Bands optimized for detection of Inner solar system objects
Can obtain Size Estimates from IR fluxes alone
2.3% albedo, 2.6 km diameter
63% albedo, 0.5 km diameter
Similar Visual Brightness
2.3% albedo, 2.6 km diameter
63% albedo, 1.6 km diameter
Similar IR Brightness

## Slide 4
WISE & Other Survey search geometries & PHAs
Current Count: 66 NEAs, giving WISE the 2nd highest discovery rate of NEOs for all the active surveys.
WISE scans
Opposition
Veres et al. 2009.
Opposition-centered ecliptic coordinates for V=22.7, H=20 (~300m) objects (simulated earth-impactors, 20yr prior to impact).

## Slide 5: MBAs
Many of the MBAs have measured optical brightness – yields albedos
Albedos can be correlated with Asteroid families
THEMIS
EOS
VESTA
FLORA
EUNOMIA
Courtesy J. Massiero

## Slide 6: Jupiter Trojans
Able to study the populations of the 2 Trojan asteroid clouds at L4 and L5
Differences in number density and albedo
Courtesy T. Grav

## Slide 7
Comet WISE Discoveries I
C/2010 G3 (WISE)
C/2010 E3 (WISE)
C/2010 D3 (WISE)
C/2010 D4 (WISE)
C/2010 D2 (WISE)
C/2010 DG56 (WISE)
P/2010 D1 (WISE)
P/2010 B2 (WISE)
Bands 2-4 three color images
WISE is an excellent means of detecting cometary dust

## Slide 8
WISE Discoveries of Cometary Activity -II
233P/La Sagra (2009 WJ50)
Bands 2-4 three color images
P/2009 WX51 (Catalina)
C/2010 FB87(Garradd-WISE)
C/2010 K2 WISE
C/2010 J4 WISE
P/2010 L1 WISE

## Slide 9: WISE Comets: Distance & Inclination
P/2010 B2
P/2010 D1
P/2010 D2
− Perihelion
− Helio. distance at Discovery
R
C/2010 D3
C/2010 E3
C/2010 DG56
C/2010 D4
C/2010 G3
C/2010 FB87
Most WISE comets are on higher-inclination orbits.
~1/4th have perihelia beyond 4AU.
~1/2 are long-period comets, 4 with nearly-parabolic orbits.
P/2010 K2
C/2010 J4
P/2010 L1

## Slide 10
Known Comets
47P/Ashbrook-Jackson
14P/Wolf
127P/Holt-Olmstead
P/Gibbs 10 (2009 S1)
Observed in varying degrees of activity
Inactive yields unambiguous nucleus size
Active yields particle size distribution & dust mass estimates
14 newly discovered comets + 68 known ≈ 82 comets observed total
12 mm
22 mm
12 mm
22 mm
67P/Churyumov-Gerasimenko

## Slide 11
WMOPS successfully identified 92% of the objects and 97% of objects reported by WMOPS were accurate (detections of only one object, with no noise points present).
What WMOPS does
Simulated truth detections mixed with 100 points of randomly added noise sources per frame.
detections extracted by WMOPS.
Notes: 2 degree by 2 degree simulated patch,
performance is worst on the perimeter
On larger patches completeness is substantially better.

## Slide 12
Moving Object Pipeline
Stationary Object Rejection & S/N & Artifact rejection
Level 1b
mdex tables & fits images
Check for Overlap Frames
Findtracklets: create new detection pairs from unreduced frames
Multiple iterations of Collapsetracklets on Overlap Frame regions
Garbage collection
Format Conversion
QA loop
SSOID match & QA filtering
Submit to MPC
Archive Preparation
QA - evaluation
SSOID input
Archive (Tracks & object-level QA products)
External pipeline input
External pipeline product
Internal pipeline product for eyes-on evaluation
Tracklet Database
Frame Database
Frame state, location, and time.
Detection time and location &
Tracklet associations
Known solar system object identification
How WMOPS does it

## Slide 13
Moving Object Pipeline
Stationary Object Rejection & S/N & Artifact rejection
Level 1b
mdex tables & fits images
Check for Overlap Frames
Findtracklets: create new detection pairs from unreduced frames
Multiple iterations of Collapsetracklets on Overlap Frame regions
Garbage collection
Format Conversion
QA loop
SSOID match & QA filtering
Submit to MPC
Archive Preparation
QA - evaluation
SSOID input
Archive (Tracks & object-level QA products)
External pipeline input
External pipeline product
Internal pipeline product for eyes-on evaluation
Tracklet Database
Frame Database
Frame state, location, and time.
Detection time and location &
Tracklet associations
Known solar system object identification
Findtracklets

## Slide 14
T1
T2
T2
T2
T2
T2
Speed Limit Boundary
T1
T2
T2
T2
T2
Tracklets
Findtracklets
Findtracklets – the starting point for tracklets
Makes all pairs that are possibly the same object based solely on sky plane speed.
Ignores all magnitude (and other possible) information.

## Slide 15
Moving Object Pipeline
Stationary Object Rejection & S/N & Artifact rejection
Level 1b
mdex tables & fits images
Check for Overlap Frames
Findtracklets: create new detection pairs from unreduced frames
Multiple iterations of Collapsetracklets on Overlap Frame regions
Garbage collection
Format Conversion
QA loop
SSOID match & QA filtering
Submit to MPC
Archive Preparation
QA - evaluation
SSOID input
Archive (Tracks & object-level QA products)
External pipeline input
External pipeline product
Internal pipeline product for eyes-on evaluation
Tracklet Database
Frame Database
Frame state, location, and time.
Detection time and location &
Tracklet associations
Known solar system object identification
Collapsetracklets

## Slide 16
T1
T2
T3
T4
Te
T1
T2
T3
T4
Two tracklets
Collapsetracklets
Collapsetracklets
Collapsetracklets
One tracklet
Collapsetracklets – the heart of WMOPS
Extrapolate positions and velocities for all tracklets to the average time in the input set
If at the average time the positions and sky plane velocities of two tracklets match, collapse the two tracklets to one tracklet.

## Slide 17
(2,3), (5,4), (9,6), (4,7), (8,1), (7,2)
KDTrees – the magic behinds Collapsetracklets
Naïve position and velocity matching would be prohibitively expensive - O(n^2)
Partition data at the median in each dimension
Cycle through dimensions
Each comparison reduces the number of candidates by 50% - O(n*log(n))

## Slide 18
Moving Object Pipeline
Stationary Object Rejection & S/N & Artifact rejection
Level 1b
mdex tables & fits images
Check for Overlap Frames
Findtracklets: create new detection pairs from unreduced frames
Multiple iterations of Collapsetracklets on Overlap Frame regions
Garbage collection
Format Conversion
QA loop
SSOID match & QA filtering
Submit to MPC
Archive Preparation
QA - evaluation
SSOID input
Archive (Tracks & object-level QA products)
External pipeline input
External pipeline product
Internal pipeline product for eyes-on evaluation
Tracklet Database
Frame Database
Frame state, location, and time.
Detection time and location &
Tracklet associations
Known solar system object identification
Findtracklets

## Slide 19
WMOPS Quality Assurance
Notes: Discovery of cometary activity in P/2009 WJ50 (La Sagra) initially in the WMOPs QA page raw image arrays

## Slide 20
WMOPS Statistics
(1/14/10-6/07/10)
Any Questions?
82
14
240
66
1159
203
80,143
15,076