## Slide 1
IPAC Energy Efficient Data Centers and Management Tools

## Slide 2: Implement Data Center Best Practices
Why Standardize?
  Necessary for HACS or CACS
Jigsaw Puzzle
  Racks need to be same
    Racks were different sizes and shapes
    Close off hot isle with containment system.
  Easy to expand or add additional rack space.
  Managing Power Distribution
    2 each power strips per rack
  A/C Placement
    APC units fit within layout.

## Slide 6: HACS vs. CACS

## Slide 7: What’s remaining to be done?
Install ceiling fans in HACS
  Why?
Relocate UPS “C”
  Why?

## Slide 9: Centralized Management Tools
Who needs them and why?
Remote Monitoring
  Alerting
    SMS “Paging”,
    MMS
    Email
    Archive
Many Managed Devices:
    5 each UPS Units 4 are 80 KVA 1 a 450 KVA unit
    17 each 10 Ton A/C Units
    6 each PDU 80 KVA each
    9 each Environmental Monitoring Devices
    108 each RPDU 2 in each rack 5 KVA
    28 each RPDU 2 in each rack 10 KVA

## Slide 18: Data Center Cooling Challenges