## Slide 1: Trends In Network Industry - Exploring Possibilities for IPAC Network
Steven Lo

## Slide 2: History
Token Rings/Thick Ethernet
  5Mbs
Shared Hubs
  10Mbs
  100Mbs
ATM
  155Mbs
Group Switching
  100Mbs
  1000Mbs

## Slide 3: Ethernet Switching and Virtual LAN
Breakthrough / ground breaking technology
Provide fault tolerance, traffic flow control and content filtering
Non-sharing, concurrent multiple connections
Solve congestion of the shared network
ASIC hardware to improve performance over software
Support virtual and private network
Software configuration, easy management
  Change system from subnet to subnet with one simple command

## Slide 4: 10 Gigabit/sec
Enabling technology
10-fold bandwidth increase over Gigabit
Gaining popular as cost reduced drastically
Server consolidation and virtualization
  Allow server to scale to larger number of processors (or VM)
Address N -> 1 congestion issue
LAN, SAN storage and cluster convergence
Currently being used by backup and clustering applications at IPAC

## Slide 5: Network-based storage
iSCSI (Internet Small Computer System Interface)
  Encapsulate SCSI command over ethernet network (TCP)
  Move from direct attach to network attach
  Single IP protocol
FCoE (Fiber Channel over Ethernet)
  Encapsulate Fiber Channel frames over ethernet network
  Unified Communication
  Simplify data center cabling
  Reduce heat and energy
  Fiber Channel will be in a catch up situation in term of speed (8Gbs vs. 10Gbs)
  10Gbs cost goes down – FC cost goes up
CEE (Converged Enhanced Ethernet) and DCB (Data Center Bridging)

## Slide 6: iSCSI
iSCSI Target Storage Device
iSCSI SAN Components
Application Server
Ethernet adapter
Ethernet Switch
Ethernet cabling
iSCSI Initiator

## Slide 7: FCoE Converged Network

## Slide 8: FCoE

## Slide 9: Converged Enhanced Ethernet (CEE)

## Slide 10: Virtualization Support
System Virtualization
  Industry predicted 50% applications will be virtualized in the next few years (by 2012)
Manage network interface becomes difficult
Each hypervisor has it’s own management scheme – no standardization
VEPA (Virtual Ethernet Port Aggregator)
  Move networking from virtual servers to dedicated Ethernet switches
  Centralize networking in dedicated equipments for better performance, security and management
  Reduce the computing overhead on virtual servers as they scale to support more virtual machines

## Slide 12: Wireless
Catching up with wired speed
Mobility is the key
802.11n
  Backward compatible with a/b/g wireless
  MIMO (Multiple Input Multiple Output)
  2 to 3 simultaneous data streams
  Standard for all modern laptops
  Over 100Mbs and can reach 300Mbs
  600Mbs is coming
  Switching controller with dumb AP (access point)
  Concurrent multiple connections

## Slide 13: What Else to Explore
40 Gigabit/sec and 100 Gigabit/sec
Wireless 802.11ad
  Gigabit Wireless (WiGig) - Wireless Gigabit Alliance
  60 GHz, short-range super-fast data transfers
Video/Audio/Data on single large pipe
InfiniBand / HPC / Clustering
Converge wired and wireless data